## Slide 1: A Guide to Orientating 3-C Geochain data using HSI devices
DISCLAIMER:
This document has been produced to serve as a general guide to appropriate HSI implementation during 3-C orientation routines. Survey and hardware/software configurations may differ to that shown in the following examples, which may in turn affect the suitability of the demonstrated rotation methodology.
Avalon Sciences Ltd (ASL) takes no responsibility for any erroneous data output as a result of following this guide. It is highly recommended to always consult your technical processing manager to QC and approve your orientation route before implementing a 3C rotation routine.

## Slide 2
HSI – HIGH SIDE INDICATOR (X-SERIES)
Introduction to HSI
leaders in BOREHOLE seismic Technology
www.avalonsciences.com/downhole-equipment/geochain
sales@avalonsciences.com
PRODUCT NAME TITLE
COMPATABLE WITH
&
Geochain Digital
Geochain EHP Digital
The new X-Series digitizer (AS272) and slim (AS251) electronics have been recently implemented with a 3C solid state inclinometer system called a High Side Indicator (HSI), which measures the direction of the pull of gravity and calculates the angles of roll and vertical inclination in each shuttle of the GeochainTM /GeochainSlim toolstring.
The integrated system denotes tool inclination from vertical (DEV Angle 0-90o) and clockwise roll looking downhole (Relative Bearing RB angle +-180o) .
Roll and inclination angles are determined from an accelerometer subsystem measuring the direction of the pull of gravity. If combined with a well deviation listing giving well azimuth trajectory (HAZI 0-360o), full 3-C processing can be achieve for all 3 components delivering a Vertical Up and Horizontal North/West field orientated dataset.
The current accuracy of the accelerometers tested for inclination measurement is ±0.1° with tool roll accuracy ±0.25° when positioned >10o from vertical.
.
Tool Rotation
Tool Roll Values exported in raw data headers – Displayed as a Well View attribute (VSProwess)
The integrated system denotes tool inclination from vertical and clockwise roll (looking downhole).
+45o
+90o
HSI Inclination
From
vertical
-90o
High Side
Mems units
Notes: 2

## Slide 3
HSI – HIGH SIDE INDICATOR (X-SERIES)
HSI for Tool QC
leaders in BOREHOLE seismic Technology
www.avalonsciences.com/downhole-equipment/geochain
sales@avalonsciences.com
PRODUCT NAME TITLE
COMPATABLE WITH
&
Geochain Digital
Geochain EHP Digital
Tool Roll Values and Inclination Values displayed during ‘Tool Monitor’ whilst tools are deployed
Real Time readout for each tool with live status reporting.
Measures tool roll and inclination for every receiver for full 3-C geophone orientation
Real time monitor read out and manual capture utility (along with internal electronics temperature)
Automatic addition of HSI data to MIRF-6 header for each individual record
Automatic calibration for optimal accuracy at various tool temperatures
The user can also manually capture the readout for all tools. (can be automatically correlated with Welltrack deviation listing in ACQ).
The high side indicator can be monitored in real time during well deployment to allow field engineer to QC tool vector fidelity and receiver-receiver roll move out.
Notes: 3

## Slide 4
AS227 Quad Pack Tap Orientation
Main Features
leaders in BOREHOLE seismic Technology
VZ
Ideal for VSP & Microseismic surveys.
Four geophones per axis.
Fits standard and high pressure ASR’s.
Greater signal to noise ratio.
Modular for quick and easy customisation.
www.avalonsciences.com/downhole-equipment/geochain
sales@avalonsciences.com
PRODUCT NAME TITLE
COMPATABLE WITH
Geochain Digital and Analogue
&
Geochain
Geochain EHP
HX
HY
Downhole
Notes: 4

## Slide 5
HSI – HIGH SIDE INDICATOR (X-SERIES)
HSI 3-C Field Processing
leaders in BOREHOLE seismic Technology
www.avalonsciences.com/downhole-equipment/geochain
sales@avalonsciences.com
PRODUCT NAME TITLE
COMPATABLE WITH
Geochain Digital
Below – Correlated raw common depth 3C stack plot in true amplitude, as recorded (no rotation applied).
The First rotation is that of the HSI roll or relative bearing (RB) angle, which is described in the plane orthogonal to the tool axis. RB is measured clockwise looking down from the vertical plane (borehole “high side” towards the direction of the arm opening Fig (a).
Above – Correlated common depth 3C stack plot in true amplitude, in geographic system, after three rotations.
The first rotation of the X,Y raw components with the highly erratic recorded HSI roll angle,
produces a great coherency between adjacent depth levels.
Notes: 5

## Slide 6
RAW DATA EXAMPLE
leaders in BOREHOLE seismic Technology
COMPATABLE WITH
Below – Correlated raw common depth 3C stack plot in true amplitude, as recorded (no rotation applied).
There are two methods in ACQ software for capturing tool roll and inclination.
HSI MIRF Header when Recording
Every time a record is taken, the HSI Roll and HSI INC values are saved to the MIRF-6 (and subsequent MIRF release) headers. Please see MIRF-6 specification for header location (https://www.avalonsciences.com/wp-content/uploads/2014/05/MIRF6-Specification.pdf) .
VSProwess X users will automatically have HSI header values imported when using ‘MIRFInput operators’.
HSI Manual Capture whilst Monitoring
A ‘Manual HSI Capture’ can be performed at any time whilst monitoring the tool string. This captures each tool Roll and Inclination value for each satellite and saves it instead to a CSV file within the acquisition job.
The user will be prompted to provide the depth of the reference tool prior to capture.
Care must be made when extracting the data to ensure appropriate HSI matching to the relevant traces.
Roll -179 to +180o or 1-360o?
The default MIRF-6 header specification stores tool roll as clockwise rotation from the tool arm pointing upwards whilst looking downhole as -179 to +180o.
However, the ‘Manual Capture’ utility allows for toggling of the HSI roll (saved to the stand alone CSV file) between -179 to +180o and 1-360o so as to allow easier infield QC.
Please take care to note the Roll angle setting. A column in the CSV will state Y/N for whether roll is 1-360o (N = Roll value stored as -179 to +180o).
VZ
HX
-HY
Notes: 6

## Slide 7
Note on Accuracy:
The current accuracy of the accelerometers tested for inclination measurement is ±0.1° with tool roll accuracy ±0.25° when tool is positioned >10o from vertical*.
*If rotating data in wells inclined steeply below this value, you may have to resort to use the coherency of seismic body waves over adjacent VSP stations, or employ a third party compass/magnetometer tool. For reference on how to do this please see (Naville et al. 2017 VSP Tool Orientation Using Magnetometer and Inclinometer Sensors. EAGE Paris Proceedings.)
a) 1st Rotation
First Rotation in RB Plane (HSI Roll Value)
Fixed 3C arrangement and polarities in ASL Geochain Tools
Relative Bearing Angle illustration in plane orthogonal to well/tool axis
[XV,YH] = Rot (RBx). [X,-Y]
Assumes use of ASR-227 or ASR-223 Fixed Sensor Pack
Step 1 – First Rotation.
[XV,YH] = Rot (RBx). [X,-Y]
Read in 3 component seismic traces from Mirf.rcd file
Reverse Polarity of second Y input component, to ( -Y )
Correct (if applicable) the HSI Tool Roll values to be 1-360o not -179 to +180o.
Apply correction of tool high side roll angle (RB) for ASR-227/ASR-223 X component offset from Arm = RBx. This will depend on the direction of X sensor with respect to the Arm direction ( RB=0 / RB origin ). In this example +135o has been applied to RB to obtain RBx.
Apply ‘left handed’ rotation, where rotation angle RBx is measured positively from first component (X) towards second component ( - Y).
(XV, YH) = [cosRBx, sinRBx;
-sinRBx, cosRBx]*(X , -Y)
XV = X * cos(RBx) - Y * sin(RBx);
YH = - X * sin(RBx) - Y * cos(RBx)
VZ
YH
XV
Well
axis
RBx = HSI Roll (1-359o) + 135o
Geochain Satellite
VZ
XV
YH

## Slide 8
Assumes use of ASR-227 or ASR-223 Fixed Sensor Pack
Step 2 – Second Rotation.
[ZV,HA] = Rot (DEV). [Z,XV]
HSI Inc Angle = ‘DEV’
Perform 2nd rotation on Z and XV components so as to correct for well deviation/Inclination angle. This can be from either HSI Well Inclination or from Well Deviation listing.
(ZV,HA) = [cos(DEV), sin(DEV);
- sin(DEV), cos(DEV)]*(Z,XV)
ZV = Z * cos(DEV) + XV * sin(DEV)
HA = - Z * sin(DEV) + XV * cos(DEV)
ZV
Well
axis
YH
HA
HA(HAZI)
ZV
XV
YH
Tool
Axis
DEV
Well Deviation
Second Rotation in Vertical Plane of Deviation (HSI Inclination Value)
Vertical Plane tangent to borehole, in Azimuth HAZI
[ZV,HA] = Rot (DEV). [Z,XV]
b) 2nd Rotation
QC Tip:
A cross normalized trace display of ZV, HA after second rotation would generally show an increase of amplitude of direct arrival on ZV relatively to Z, and a decrease of amplitude on HA relatively to XV, in a deviated well / rig source VSP.
ZV
HA
YH
Cross-normalized 3C display =
3C constant gain at each depth level

## Slide 9
Assumes use of ASR-227 or ASR-223 Fixed Sensor Pack
Step 3 – Third Rotation.
[HN,HW] = Rot (HAZI). [HA,YH]
Well Track Azimuth = ‘HAZI’
Perform 3rd rotation on HA and YH components to correct for well azimuth angle in order to output components relative to North. The vertical ZV component points upwards.
(HN,HW) = [cos(HAZI), sin(HAZI);
- sin(HAZI), cos(HAZI)]*(HA,YH)
HN = HA*cos(HAZI) + YH*sin(HAZI)
HW= -HA*sin(HAZI) + YH*cos(HAZI)
ZV
Well
axis
HW
HN
YH
HN
North
HW
West
HA(HAZI)
HAZI = Hole
Azimuth
Well head
+
G
Third Rotation in Horizontal Plane (From Well Listing)
Horizontal Plane, Looking Down
[HN,HW] = Rot (HAZI). [HA,YH]
c) 3rd Rotation
ZV
HN
HW
Cross-normalized 3C display =
3C constant gain at each depth level

## Slide 10
EULER angles: https://en.wikipedia.org/wiki/Euler_angles
Naville, C., Serbutoviez, S. and Lecomte, J. [2012] Method for time picking and orientation of three-component seismic signals in wells; Patent US2012_0046871A1
Wills, W., Naville, C., and Nott-Bower, M. Tubridy, G. [2017] Orientation if a 3-C VSP dataset acquired by integrated geophone sensor and MEMS inclinometer devices; 3C VSP orientation field QC. Fourth EAGE BGW Abu Dhabi Proceedings 2017.
References